## Slide 1: Embedded Software Essentials
Introduction to Build Systems using GNU Toolsets
C1 M2 V1

## Slide 2: Copyright
Copyright (C) 2017 by Alex Fosdick. Redistribution, modification or use of this presentation is permitted as long as the files maintain this copyright. Users are permitted to modify this and use it to learn about the field of embedded software. Alex Fosdick and the University of Colorado are not liable for any misuse of this material.

## Slide 3: Embedded System Development Platform
Print Circuit Board (PCB)
Processor(s)
External Hardware
Power
Programmer Debugger
Host Machine
Internal Memory
Code
External Hardware
External Hardware
SW Tools
The host machine contains our Build Environment

## Slide 4: Build Environment
Host Machine
Code
Software Tools
Software Engineer’s Tools include Compiler Toolchain
GCC – GNU’s Compiler Collection
Make
Executable
The host machine contains our Build Environment

## Slide 5: Software Tools
Software Tools
Source Files usually mostly in High Level Languages
*.c
*.c
*.c
*.h
Compiler Toolchain
Executable File
Version Control
Executable
Loader
IDE
Compiler Toolchain
Architecture Specific Machine Code

## Slide 6: Building a Software Project
C-Programming
(High Level Language)
ARM Assembly Language (Low Level Language)[1]
Machine Code
(Binary encoded Assembly Instructions) [2]
int x = 0;
int y = 20;
int z = 5;
…
while (y >= z) {
y = y – z;
x++;
}
ldr r2, (y)
ldr r3, (z)
ldr r4, (x)
LOOP:
sub r2, r3
inc r4
cmp r2, r3
bgt LOOP
str r2, (y)
str r4, (x)
0x0c1b
0x7023
0x2302
0x71bb
0x2300
0xf7ff ef24
0xc407
0x8023
0x3402
[1] (x),(y),(z) = Pseudocode
[2] Machine code just an example
Notes: Emphasize differences between an MCU and a Embedded OS

## Slide 7: Building a Software Project
Build and Install Process:
  Preprocessing
  Assembling
  Compiling
  Linking
  Locating
  Installing
Installation will require other tools
Compiler Toolset
Preprocessor
Assembler
Linker
Locator
Loader
Compiler
Notes: Emphasize differences between an MCU and a Embedded OS

## Slide 8: Build Process (linear)
Source Files
*.c
*.c
*.c/*.h
Compiler
Proper
Object Files
Preprocessor
Preprocessed Files
*.c
*.c
*.i
*.c
*.c
*.s
Assembler
*.c
*.c
*.o
Assembly Files
Linker
Locator
Relocatable File
Executable

## Slide 9: Compilation (No Linking)
Source Files
*.c
*.c
*.c
*.h
Object Files
Compiler
*.c
*.c
*.o
*.c
*.c
*.s
Object Files
Assembler
*.c
*.c
*.o
Source Files
*.c
*.c
*.c/*.h
Compiler
Proper
Object Files
Preprocessor
Preprocessed Files
*.c
*.c
*.i
*.c
*.c
*.s
Assembler
*.c
*.c
*.o
Assembly Files
Assembly Files

## Slide 10: Compilation (No Linking)
Source Files
*.c
*.c
*.c
*.h
Object Files
Compiler
*.c
*.c
*.o
*.c
*.c
*.s
Object Files
Assembler
*.c
*.c
*.o
Source Files
*.c
*.c
*.c/*.h
Compiler
Proper
Object Files
Preprocessor
Preprocessed Files
*.c
*.c
*.i
*.c
*.c
*.s
Assembler
*.c
*.c
*.o
Assembly Files
Assembly Files

## Slide 11: Native Compilation
Compile an executable on one system and it is intended to run on same system
Personal Computer (Windows/Linux)
Executable
File
Native Compiler and Linker (GCC)
*.c
*.c
*.c
*.h
No hardware needed

## Slide 12: Cross Compilation
Compile an executable on one system and it is intended to run on another
Embedded System
Personal Computer (Windows/Linux)
Programmer
Executable
File
Processor
Flash
Cross Compiler and Linker (GCC)
*.c
*.c
*.c
*.h
Programmer HW needed for Install

## Slide 13: Cross Compilation
Installer tool sends executable to on board programmer
  No external hardware needed
Personal Computer (Windows/Linux)
Executable
File
Embedded System
Processor
On-Board Programmer
Flash
Cross Compiler and Linker (GCC)
Installer Tool
*.c
*.c
*.c
*.h

## Slide 14: Compiler Toolchain
GCC = GNU’s Compiler Collection
  Contains many tools (compiler, assembler, linker, etc)
GNU Make
  “Tool that controls the generation of executables and other non-source files of a program from the program’s source files”[2]
Software Tools
Source Files usually mostly in High Level Languages
*.c
*.c
*.c
*.h
Compiler Toolchain
Executable File
Version Control
Executable
Loader
IDE
Compiler Toolchain
Architecture Specific Machine Code