## Slide 1: Embedded Software Essentials
The Preprocessor
C1 M2 V3

## Slide 2: Copyright
Copyright (C) 2017 by Alex Fosdick. Redistribution, modification or use of this presentation is permitted as long as the files maintain this copyright. Users are permitted to modify this and use it to learn about the field of embedded software. Alex Fosdick and the University of Colorado are not liable for any misuse of this material.

## Slide 3: The Preprocess [S1.2.3.1]
First Step In Build Process
Source Files
*.c
*.c
*.c/*.h
Compiler
Proper
Object Files
Preprocessor
Preprocessed
Files
*.c
*.c
*.i
*.c
*.c
*.s
Assembler
*.c
*.c
*.o
Assembly Files
Linker
Locator
Relocatable File
Executable

## Slide 4: Preprocessor Directives [S1.2.3.2]
Special keywords used by the preprocessor before compilation
   Compile Time switches
Directives start with ‘#’ sign
Important Directives
  #define, #undef
  #ifndef, #ifdef, #endif
  #include
  #warning, #error
  #pragma

## Slide 5: Preprocessor’s Role [S1.2.3.3.a]
† = The preprocessor is bundled with the compiler
Compiler (gcc)†
Source Files
*.c
*.c
*.c/*.h
Compiler
Proper
Object Files
Preprocessor
Preprocessed Files
*.c
*.c
*.i
*.c
*.c
*.o
To Linker
*.c
*.c
*.i
Output with –E option

## Slide 6: Preprocessed Output [S1.2.3.3.b]
Stop after preprocessing
Output the preprocessed file to a *.i extension
$ gcc -E -o main.i main.c

## Slide 7: #define as a Constant [S1.2.3.4]
Used for defining constants, features or macro functions
Constant Examples:
#define LENGTH (10)
#define NO_ERROR (0)
#define ERROR (1)
/* Macro defined as another macro */
#define UART_ERROR ERROR
#define <MACRO-NAME> <MACRO-VALUE>

## Slide 8: Macro Substitution [S1.2.3.5a]
#define ZERO (0)
#define LENGTH (10)
int main(){
char arr[LENGTH];
memset(arr, ZERO, LENGTH);
…
return 0;
}
int main(){
char arr[10];
memset(arr, 0, 10);
…
return 0;
}
Preprocessor
After Preprocessing
Original File

## Slide 9: Macro Substitution [S1.2.3.5b]
#define ZERO (0)
#define LENGTH (10)
int main(){
char arr[LENGTH];
memset(arr, ZERO, LENGTH);
…
return 0;
}
int main(){
char arr[10];
memset(arr, 0, 10);
…
return 0;
}
Preprocessor
After Preprocessing
Original File

## Slide 10: #define as a Macro Function [S1.2.3.6]
Provide Macro Function name, parameters, and operation
Constant Examples:
#define <MACRO-FUNCTION>(<PARAMS>) (<OPERATION>)
#define SQUARE(x) (x*x)
…
int y_sqrd;
int y = 2;
y_square = SQUARE(y);
 y_square will equal 4

## Slide 11: Macro Function Substitution [S1.2.3.7a]
#define SQUARE(x) (x*x)
int main(){
int y_sqrd;
int y = 2;
y_square = SQUARE(y);
return 0;
}
int main(){
int y_sqrd;
int y = 2;
y_square = (y*y);
…
return 0;
}
Preprocessor
After Preprocessing
Original File

## Slide 12: Macro Function Substitution [S1.2.3.7b]
#define SQUARE(x) (x*x)
int main(){
int y_sqrd;
int y = 2;
y_square = SQUARE(y);
return 0;
}
int main(){
int y_sqrd;
int y = 2;
y_square = (y*y);
…
return 0;
}
Preprocessor
After Preprocessing
Original File

## Slide 13: Macro Function Issues [S1.2.3.8a]
#define SQUARE(x) (x*x)
int main(){
int y_sqrd;
int y = 2;
y_square = SQUARE(y++);
return 0;
}
int main(){
int y_sqrd;
int y = 2;
y_square = (y++*y++);
…
return 0;
}
Preprocessor
After Preprocessing
Original File

## Slide 14: Macro Function Issues [S1.2.3.8b]
#define SQUARE(x) (x*x)
int main(){
int y_sqrd;
int y = 2;
y_square = SQUARE(y++);
return 0;
}
int main(){
int y_sqrd;
int y = 2;
y_square = (y++*y++);
…
return 0;
}
Preprocessor
After Preprocessing
Original File
Undefined Behavior!!!
After the line y_square executes:
y = 4
y_square = 6
Notes: If num = 2, after num = 4, y = 6

## Slide 15: #define/#undef as a Feature [S1.2.3.9]
Directive used for Boolean Compilation Conditions
Constant Examples:
/* Define feature for the MSP */
#define MSP_PLATFORM
#define TEN (10)
/* Undefine the Constant TEN */
#undef TEN
#define <FEATURE-NAME>
#define KL25_PLATFORM
/* Undefine the Feature */
#undef KL25_PLATFORM

## Slide 16: #if-else Directives [S1.2.3.10]
Conditionally compile blocks of code
  #ifdef
  #ifndef
  #elif
  #else
  #endif – End of block (required)
Useful for debugging
“Turn Off” Large amounts of code
#define COMPILE_CODE
…
#ifdef COMPILE_CODE
// Code will be compiled
#endif
#define DO_NOT_COMPILE_CODE
…
#undef DO_NOT_COMPILE_CODE
#ifdef DO_NOT_COMPILE_CODE
// Code will be NOT be compiled
#endif

## Slide 17: #if-else & #define Directives [S1.2.3.11]
int main(void){
#ifdef ( KL25_PLATFORM ) && ( ! MSP_PlATFROM )
kl25_initialize();
#elif ( MSP_PlATFROM ) && ( ! KL25_PLATFORM )
msp_initialize();
#else
#error “Please specify one platform target”
#endif
/* More code here */
return 0;
}

## Slide 18: #include Directive [S1.2.3.12]
Includes software defined in other files
Declarations get copied into file
Include file from local directory
#include “uart.h”
Include file from a library path or include path:
#include <stdio.h>

## Slide 19: #include Directive [S.1.2.3.13a]
#include “my_file.h”
char arr[LENGTH];
void clear(char * ptr, int size){
int i;
for(i = 0, i < size, i++){
ptr[i] = 0;
}
}
void clear(char * ptr, int size);
char arr[10];
void clear(char * ptr, int size){
int i;
for(i = 0, i < size, i++){
ptr[i] = 0;
}
}
my_file.i
my_file.c
#define LENGTH (10)
void clear(char * ptr, int size);
my_file.h
Preprocessed

## Slide 20: #include Directive [S.1.2.3.13b]
#include “my_file.h”
char arr[LENGTH];
void clear(char * ptr, int size){
int i;
for(i = 0, i < size, i++){
ptr[i] = 0;
}
}
void clear(char * ptr, int size);
char arr[10];
void clear(char * ptr, int size){
int i;
for(i = 0, i < size, i++){
ptr[i] = 0;
}
}
my_file.i
my_file.c
#define LENGTH (10)
void clear(char * ptr, int size);
my_file.h
Preprocessed

## Slide 21: #pragma [S1.2.3.14]
Gives a specific instruction to the compiler
  Controls compilation from software instead of command line
Implementation/Compiler specific  Unrecognized pragmas will be ignored
Adds options to compiler for specific function
#pragma GCC push_options
Causes an error during compilation if code uses these functions
#pragma GCC poison printf sprint fprintf
Compile a function with a specific architecture
#pragma GCC target (“arch=armv6”) -or-
(“cpu=cortex-m0plus”)

## Slide 22: Pragma Compile Failure [S1.2.3.15]

## Slide 23: Compile Time Switch [S1.2.3.16]
Condition provided at Compile time to dictate WHAT should be compiled
  Uses combination of #if-else and #define directives
#if defined ( KL25Z_PLATFORM ) && ! defined ( MSP_PLATFROM )
kl25_initialize();
#elif ( MSP_PLATFROM ) && ( ! KL25Z_PLATFORM )
msp_initialize();
#else
#error “Please specify one platform target”
#endif

## Slide 24: Compile Time Switch [S1.2.3.17]
Condition provided at Compile time to dictate WHAT should be compiled
  Uses combination of #if-else and #define directives
Compiler (gcc)
Source Files
*.c
*.c
*.c/*.h
Preprocessor
*.c
*.c
*.i
To Compiler Proper
$ gcc –DMSP_PLATFORM –o main.out main.c
–D<MACRO-NAME>
Add extra option to gcc command to define Macro

## Slide 25: Compile Time Switch [S1.2.3.18a]
KL25z
UART Peripheral Module
GPIO HW
UART Connected Device
UART_Lib (KL25z)
Device_Lib
Application
Each has unique Hardware and Firmware configuration
MSP432
UART Peripheral Module
GPIO HW
UART_Lib (MSP432)
Device_Lib
Application
UART Connected Device

## Slide 26: Compile-Time Switch [S1.2.3.18b]
#ifdef KL25Z_PLATFORM && ...
#include “kl25_uart.h”
#elif MSP_PLATFORM && ...
#include “msp_uart.h”
#else
…
#endif
KL25z
UART Peripheral Module
GPIO HW
UART Connected Device
KL25z Executable Program
MSP432
UART Peripheral Module
GPIO HW
UART Connected Device
MSP432 Executable Program
Software Repository
UART_Lib (KL25z)
Device_Lib.c/.h
Application.c/.h
UART_Lib (MSP432)
*.c
*.c
*.c
*.h
Compiler & Linker
Executable

## Slide 27: Compile-Time Switch [Fig 1.2.3.18c]
Software Repository
KL25z
UART Peripheral Module
GPIO HW
UART Connected Device
KL25z Executable Program
MSP432
UART Peripheral Module
GPIO HW
UART Connected Device
MSP432 Executable Program
UART_Lib (KL25z)
Device_Lib.c/.h
Application.c/.h
UART_Lib (MSP432)
$ gcc -DKL25Z_PLATFORM –c Device_lib.c …
Compiler & Linker
#ifdef KL25Z_PLATFORM && ...
#include “kl25_uart.h”
#elif MSP_PLATFORM && ...
#include “msp_uart.h”
#else
…
#endif

## Slide 28: Compile-Time Switch [Fig 1.2.3.18d]
Software Repository
KL25z
UART Peripheral Module
GPIO HW
UART Connected Device
KL25z Executable Program
MSP432
UART Peripheral Module
GPIO HW
UART Connected Device
MSP432 Executable Program
UART_Lib (KL25z)
Device_Lib.c/.h
Application.c/.h
UART_Lib (MSP432)
Compiler & Linker
$ gcc -DMSP_PLATFORM –c Device_lib.c …
#ifdef KL25Z_PLATFORM && ...
#include “kl25_uart.h”
#elif MSP_PLATFORM && ...
#include “msp_uart.h”
#else
…
#endif

## Slide 29: Preprocessor Command Line Define [Unused]
Compiler (gcc)
Source Files
*.c
*.c
*.c/*.h
Preprocessor
*.c
*.c
*.i
To Compiler Proper
$ gcc –DMSP_PLATFORM –o main.out main.c
–D<MACRO-NAME>
Add extra option to gcc command line to define Macro