## Slide 1: Embedded Software Essentials
Linkers
C1 M2 V5

## Slide 2: Copyright
Copyright (C) 2017 by Alex Fosdick. Redistribution, modification or use of this presentation is permitted as long as the files maintain this copyright. Users are permitted to modify this and use it to learn about the field of embedded software. Alex Fosdick and the University of Colorado are not liable for any misuse of this material.

## Slide 3: Linking and Locating [S1]
Last steps In Build Process
Source Files
*.c
*.c
*.c/*.h
Compiler
Proper
Object Files
Preprocessor
Preprocessed
Files
*.c
*.c
*.i
*.c
*.c
*.s
Assembler
*.c
*.c
*.o
Assembly Files
Linker
Locator
Relocatable File
Executable

## Slide 4: Typical Build Process [S2]
Linking and Locating
Source Files
Compiler
Object Files
Linker
Locator
Relocatable File
Executable
Assembler
Linker File
*.c
*.c
*.c
*.h
*.c
*.c
*.s
*.c
*.c
*.o
*.c
*.c
*.o
*.c
*.c
*.a
Library
Files
Linker File Option with
–T flag
$ gcc main.c –o main.out
$ gcc main.c –o main.out –Xlinker –T linker_file.lds
$ gcc main.c –o main.out –Wl,–T,linker_file.lds

## Slide 5: Linkers [S3a]
Liking and Locating (ld)
Combines all of objects files into a single executable
  Object code uses symbols to reference other functions/variables
Linker
Locator
Relocatable File
Executable
Linker File
*.c
*.c
*.o
*.a
$ gcc –o main.out main.c
Invoke the linker indirectly from compiler (and with no options)
Input with –T option
Notes: Static = everything is compiled and copied into the executable
Dynamic = Linking is done at runtime with symbols referred in the runtime libraries

## Slide 6: Linkers [S3b]
Liking and Locating (ld)
Combines all of objects files into a single executable
  Object code uses symbols to reference other functions/variables
Linker
Locator
Relocatable File
Executable
Linker File
*.c
*.c
*.o
*.a
$ gcc –o main.out main.c
Invoke the linker indirectly from compiler (and with no options)
Input with –T option
Cannot be executed
11001000011010010101101100111101
main.o
01101010101011101011100010101000
memory.o
Notes: Static = everything is compiled and copied into the executable
Dynamic = Linking is done at runtime with symbols referred in the runtime libraries

## Slide 7: Linking Object Files [S4a]
#ifndef __MEMORY_H__
#define __MEMORY_H__
char memzero(char * src, int length);
#endif /* __MEMORY_H__ */
#include “memory.h”
char memzero(char * src, int length){
int i;
for(i = 0; i < length; i++){
*src++ = 0;
}
}
main.c
memory.h
#include “memory.h”
int main(){
char arr[10];
memzero(arr, 10);
return 0;
}
memory.h
Three source files (*.h & *.c)
Must convert *.c files into object code

## Slide 8: Linking Object Files [S4b]
#ifndef __MEMORY_H__
#define __MEMORY_H__
char memzero(char * src, int length);
#endif /* __MEMORY_H__ */
#include “memory.h”
char memzero(char * src, int length){
int i;
for(i = 0; i < length; i++){
*src++ = 0;
}
}
main.c
memory.h
#include “memory.h”
int main(){
char arr[10];
memzero(arr, 10);
return 0;
}
memory.h
The object files have many symbols that need to be tracked and resolved

## Slide 9: Linking Object Files [S4c]
11001000011010010101101100111101
main.o
01101010101011101011100010101000
memory.o
After compilation, we have 2 object files (header file provide symbol reference)
main.o has references to symbols defined in memory.o
memory.o has the definitions of these special symbols
Object files are NOT human readable
Symbol tables track important references

## Slide 10: Linking Object Files [S4d]
#ifndef __MEMORY_H__
#define __MEMORY_H__
char memzero(char * src, int length);
#endif /* __MEMORY_H__ */
#include “memory.h”
char memzero(char * src, int length){
int i;
for(i = 0; i < length; i++){
*src++ = 0;
}
}
main.c
memory.h
#include <stdlib.h>
int main(){
char a[10], b[10];
memmove(a, b, 10);
return 0;
}
memory.h
Function memmove is not defined in included files
Causes an error
???

## Slide 11: Libraries [S6a]
Linker must know name and path to library to link with it
  Static and Dynamic libraries get linked at different points
Linker & locator
Executable
*.c
*.c
*.o
Input with –l and –L option
Cannot be executed
*.c
*.c
libs
11001000011010010101101100111101
main.o
01101010101011101011100010101000
memory.o
Static Libraries
Compiled Time Linked
Some references to library symbols
Notes: Static = everything is compiled and copied into the executable
Dynamic = Linking is done at runtime with symbols referred in the runtime libraries

## Slide 12: Libraries [S6b]
Linker must know name and path to library to link with it
  Static and Dynamic libraries get linked at different points
Linker & locator
Executable
*.c
*.c
*.o
Cannot be executed
*.c
*.c
libs
11001000011010010101101100111101
main.o
01101010101011101011100010101000
memory.o
Shared Libraries
Input with –l and –L option
Runtime Linked
Some references to library symbols
Notes: Static = everything is compiled and copied into the executable
Dynamic = Linking is done at runtime with symbols referred in the runtime libraries

## Slide 13: Linking Object Files [S7]
main.c
#include <stdlib.h>
#include <stdio.h>
int main(){
char arr[10];
printf(“Hello World\n”);
return 0;
}
How do we enter main?
How do we exit or return from main?
Standard libraries can be statically or dynamically linked
Entry and exit points from main are included in a standard library that is automatically included by the linker
Can stop auto link of standard libs with –nostdlib flag

## Slide 14: Linking Object Files [S8]
Relocatable file
main:0110101010101110101(memzero)1100010101000
memzero:11001000011010010101101100111101
After linking, we have 1 object files, and the symbols between the two are resolved
Relocatable & Executable files are NOT human readable
Linker
Locator
Relocatable File
Executable
*.c
*.c
*.o
*.a
Variables and Functions are represented by symbols

## Slide 15: Linking Object Files [S9]
Executable file
0x7c:0110101010101110101 (0x100)1100010101000
0x100:11001000011010010101101100111101
After locating, symbols are removed and direct addresses get assigned into the object code
The processor understands machine code (binary encoded instructions). These must have direct references to memory (addresses, not symbols)
Variables and Functions have been replaced with addresses
Linker & locator
Executable
*.c
*.c
*.o
*.c
*.c
libs
Linker File

## Slide 16: Linker Files [S10]
Microcontroller
GPIO
Flash
CPU
Peripherals
SRAM
Linker & locator
Executable
*.c
*.c
*.o
*.c
*.c
libs
Linker File
Details on how to map compiled data into physical memory regions
???

## Slide 17: Linker Scripts Details [S11]
Code sections to memory regions map
Start and Sizes of memory regions
Access attributes of memory regions
Report checking for over-allocation
Entry points of the program
Example code/data sections:
  .bss
  .data
  .text
  .isr_vectors
  .heap
Example Memory Regions:
  RAM/SRAM
  FLASH (MAIN)
  EEPROM
  VECTORS
  BOOTLOADER
Entry Point Example:
ENTRY(Reset_Handler)
Linker & locator
Executable
*.c
*.c
*.o
*.c
*.c
libs
Linker File

## Slide 18: Example Linker Script Contents [S12a]
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Physical Memory Regions
Compiled Memory Sections

## Slide 19: Example Linker Script Contents [S12b]
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
Each “code” section output from compilation is then mapped into memory regions
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Physical Memory Regions
Compiled Memory Sections

## Slide 20: Example Linker Script Contents [S12c]
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
Specifies the location the compiled region should map into physical memory
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Physical Memory Regions
Compiled Memory Sections

## Slide 21: Example Linker Script Contents [S12c]
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Specifies the location the compiled region should map into physical memory
This is the “relocating” that the locator does
Physical Memory Regions
Compiled Memory Sections

## Slide 22: Example Linker Script Contents [S12d]
Specifies the location the compiled region should map into physical memory
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Physical Memory Regions
Compiled Memory Sections
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}

## Slide 23: Example Linker Script Contents [S12e]
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
Specifies the start address and length of the region for the memory map (in bytes)
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Physical Memory Regions
Compiled Memory Sections

## Slide 24: Example Linker Script Contents [S12e]
HEAP_SIZE = DEFINED(__heap_size__) ? __heap_size__ : 0x0400;
STACK_SIZE = DEFINED(__stack_size__) ? __stack_size__ : 0x0800;
__StackTop = ORIGIN(SRAM_DATA) + LENGTH(SRAM_DATA);
__StackLimit = __StackTop - STACK_SIZE;
ASSERT(__StackLimit >= __HeapLimit, “Region SRAM_DATA overflowed!")
Linker file can calculate memory segments
  Can throw an errors if memory space is invalid

## Slide 25: Example Linker Script Contents [S12c]
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
Specifies the location the compiled region should map into physical memory
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Physical Memory Regions
Compiled Memory Sections

## Slide 26: Example Linker Script Contents [S12f]
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
Specifies the access properties of the region
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Physical Memory Regions
Compiled Memory Sections

## Slide 27: Memory Segments [S13a]
Code Memory
Start Address
Start Address
End Address
End Address
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Data Memory
(unused)
(unused)

## Slide 28: Memory Segments [S13b]
Code Memory (MAIN)
Start Address
(0x20000000)
Start Address
(0x00000000)
End Address
(0x00040000)
End Address
(0x20010000)
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
Data Memory (SRAM_DATA)
(unused)
(unused)

## Slide 29: Memory Segments [S13c]
Code Memory (MAIN)
Start Address
(0x20000000)
Start Address
(0x00000000)
End Address
(0x00040000)
End Address
(0x20010000)
MEMORY
{
MAIN (RX) : origin = 0x00000000, length = 0x00040000
SRAM_DATA (RW) : origin = 0x20000000, length = 0x00010000
}
SECTIONS
{
.intvecs: > 0x00000000
.text : > MAIN
.const : > MAIN
.cinit : > MAIN
.pinit : > MAIN
.data : > SRAM_DATA
.bss : > SRAM_DATA
.heap : > SRAM_DATA
.stack : > SRAM_DATA (HIGH)
}
.text
.intvecs
.data
.bss
.const
(unused)
.heap
.stack
.cinit
.pinit
(unused)
Data Memory (SRAM_DATA)

## Slide 30: Linker Flags [S14a]
Option & Format | Purpose
-map [NAME] | Outputs a memory map file [NAME] from the result of linking
-T [NAME] | Specifies a linker script name [NAME]
-o [NAME] | Place the output in the filename [NAME]
-0<#> | The level of optimizations from [#=0-3] (-O0, -O1, -O2, -O3)
-Os | Optimize for memory size
-z stacksize=[SIZE] | The amount of stack space to reserve
-shared | Produce a shared library (dynamic linking library)
-l[LIB] | Link with library
-L[DIR] | Include the following library path
-Wl,<OPTION> | Pass option to linker from compiler
-Xlinker <OPTION> | Pass option to linker from compiler

## Slide 31: Passing Flags to Linker from Compiler [S14b]
You can pass arguments from the compiler to the linker
$ gcc <other-options-here> -Xlinker –Map=main.map
$ gcc <other-options-here> -Xlinker –T=mkl25z_lnk.ld
$ gcc <other-options-here> -Wl,option
$ gcc <other-options-here> -Wl,-Map,main.map
$ gcc <other-options-here> -Wl,-Map=main.map
Notes: Static = everything is compiled and copied into the executable
Dynamic = Linking is done at runtime with symbols referred in the runtime libraries

## Slide 32: Executable File Formats [S15]
Executable and Linkable Format (ELF)
Common Object File Format (COFF)
Intel Hex Record
Motorola S Record (SREC)
ARM Image Format (AIF)
Intel Hex Record Example File[3]
ELF File Example[4]