## Slide 1: Embedded Software Essentials
Make
C1 M2 V6

## Slide 2: Copyright
Copyright (C) 2017 by Alex Fosdick. Redistribution, modification or use of this presentation is permitted as long as the files maintain this copyright. Users are permitted to modify this and use it to learn about the field of embedded software. Alex Fosdick and the University of Colorado are not liable for any misuse of this material.

## Slide 3: Building Manually [S1a]
Building can be tedious
  Many GCC flags
  Many independent commands
  Many build targets
  Many supported architectures
  Many source files
Building manually can
  Cause Consistency issues
  Waste development time
Linux Kernel Example
  *.c Files: 23,000+
  *.h Files: 18,000+
  *.S Files: 1,400+

## Slide 4: Building Manually [S1b]
Building can be tedious
  Many GCC flags
  Many independent commands
  Many build targets
  Many supported architectures
  Many source files
Building manually can
  Cause Consistency issues
  Waste development time
Manually compiling each file and linking is NOT scalable for large software projects or large teams
Large chance for human error

## Slide 5: Example Compile in KDS [S2a]
12:27:47 **** Build of configuration Debug for project project2 ****
make all
Building file: ../Sources/main.c
Invoking: Cross ARM C Compiler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -DTIMER_INTERRUPT=0 -I"../Sources" -I"../Includes" -std=c99 -MMD -MP -MF"Sources/main.d" -MT"Sources/main.o" -c -o "Sources/main.o" "../Sources/main.c"
Finished building: ../Sources/main.c
Building file: ../Sources/memory.c
Invoking: Cross ARM C Compiler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -DTIMER_INTERRUPT=0 -I"../Sources" -I"../Includes" -std=c99 -MMD -MP -MF"Sources/memory.d" -MT"Sources/memory.o" -c -o "Sources/memory.o" "../Sources/memory.c"
Finished building: ../Sources/memory.c
Building file: ../Project_Settings/Startup_Code/startup_MKL25Z4.S
Invoking: Cross ARM GNU Assembler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -x assembler-with-cpp -MMD -MP -MF"Project_Settings/Startup_Code/startup_MKL25Z4.d" -MT"Project_Settings/Startup_Code/startup_MKL25Z4.o" -c -o "Project_Settings/Startup_Code/startup_MKL25Z4.o" "../Project_Settings/Startup_Code/startup_MKL25Z4.S"
Finished building: ../Project_Settings/Startup_Code/startup_MKL25Z4.S
Building file: ../Project_Settings/Startup_Code/system_MKL25Z4.c
Invoking: Cross ARM C Compiler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -DTIMER_INTERRUPT=0 -I"../Sources" -I"../Includes" -std=c99 -MMD -MP -MF"Project_Settings/Startup_Code/system_MKL25Z4.d" -MT"Project_Settings/Startup_Code/system_MKL25Z4.o" -c -o "Project_Settings/Startup_Code/system_MKL25Z4.o" "../Project_Settings/Startup_Code/system_MKL25Z4.c"
Finished building: ../Project_Settings/Startup_Code/system_MKL25Z4.c
Building target: project2.elf
Invoking: Cross ARM C++ Linker
arm-none-eabi-g++ -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -T "MKL25Z128xxx4_flash.ld" -Xlinker --gc-sections -L"C:/classes/boulder/ECEN5013/Spring2016/kds_wksp/project2/Project_Settings/Linker_Files" -Wl,-Map,"project2.map" -specs=nano.specs -specs=nosys.specs -o "project2.elf" ./Sources/main.o ./Sources/memory.o ./Project_Settings/Startup_Code/startup_MKL25Z4.o ./Project_Settings/Startup_Code/system_MKL25Z4.o
Finished building target: project2.elf
12:27:49 Build Finished (took 1s.659ms)
Project for a KL25z Platform with a Cortex-M0+with containing 2 Source files and some startup Files

## Slide 6: Example Compile in KDS [S2b]
12:27:47 **** Build of configuration Debug for project project2 ****
make all
Building file: ../Sources/main.c
Invoking: Cross ARM C Compiler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -DTIMER_INTERRUPT=0 -I"../Sources" -I"../Includes" -std=c99 -MMD -MP -MF"Sources/main.d" -MT"Sources/main.o" -c -o "Sources/main.o" "../Sources/main.c"
Finished building: ../Sources/main.c
Building file: ../Sources/memory.c
Invoking: Cross ARM C Compiler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -DTIMER_INTERRUPT=0 -I"../Sources" -I"../Includes" -std=c99 -MMD -MP -MF"Sources/memory.d" -MT"Sources/memory.o" -c -o "Sources/memory.o" "../Sources/memory.c"
Finished building: ../Sources/memory.c
Building file: ../Project_Settings/Startup_Code/startup_MKL25Z4.S
Invoking: Cross ARM GNU Assembler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -x assembler-with-cpp -MMD -MP -MF"Project_Settings/Startup_Code/startup_MKL25Z4.d" -MT"Project_Settings/Startup_Code/startup_MKL25Z4.o" -c -o "Project_Settings/Startup_Code/startup_MKL25Z4.o" "../Project_Settings/Startup_Code/startup_MKL25Z4.S"
Finished building: ../Project_Settings/Startup_Code/startup_MKL25Z4.S
Building file: ../Project_Settings/Startup_Code/system_MKL25Z4.c
Invoking: Cross ARM C Compiler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -DTIMER_INTERRUPT=0 -I"../Sources" -I"../Includes" -std=c99 -MMD -MP -MF"Project_Settings/Startup_Code/system_MKL25Z4.d" -MT"Project_Settings/Startup_Code/system_MKL25Z4.o" -c -o "Project_Settings/Startup_Code/system_MKL25Z4.o" "../Project_Settings/Startup_Code/system_MKL25Z4.c"
Finished building: ../Project_Settings/Startup_Code/system_MKL25Z4.c
Building target: project2.elf
Invoking: Cross ARM C++ Linker
arm-none-eabi-g++ -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -T "MKL25Z128xxx4_flash.ld" -Xlinker --gc-sections -L"C:/classes/boulder/ECEN5013/Spring2016/kds_wksp/project2/Project_Settings/Linker_Files" -Wl,-Map,"project2.map" -specs=nano.specs -specs=nosys.specs -o "project2.elf" ./Sources/main.o ./Sources/memory.o ./Project_Settings/Startup_Code/startup_MKL25Z4.o ./Project_Settings/Startup_Code/system_MKL25Z4.o
Finished building target: project2.elf
12:27:49 Build Finished (took 1s.659ms)
Project for a KL25z Platform with a Cortex-M0+with containing 2 Source files and some startup Files

## Slide 7: Example Compile in KDS [S3]
Each compile, assemble and link command are
  More then 100 Characters
  More then 10 Flags
Building file: ../Sources/main.c
Invoking: Cross ARM C Compiler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -I"../Sources" -I"../Includes" -std=c99 -MMD -MP -MF"Sources/main.d" -MT"Sources/main.o" -c -o "Sources/main.o" "../Sources/main.c"
Building file: ../Project_Settings/Startup_Code/startup_MKL25Z4.S
Invoking: Cross ARM GNU Assembler
arm-none-eabi-gcc -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -x assembler-with-cpp -MMD -MP -MF"Project_Settings/Startup_Code/startup_MKL25Z4.d" -MT"Project_Settings/Startup_Code/startup_MKL25Z4.o" -c -o "Project_Settings/Startup_Code/startup_MKL25Z4.o" "../Project_Settings/Startup_Code/startup_MKL25Z4.S"
Building target: project.elf
Invoking: Cross ARM C++ Linker
arm-none-eabi-g++ -mcpu=cortex-m0plus -mthumb -O0 -fmessage-length=0 -fsigned-char -ffunction-sections -fdata-sections -g3 -T "MKL25Z128xxx4_flash.ld" -Xlinker --gc-sections -L"C:/coursera/kds_wksp/project2/Project_Settings/Linker_Files" -Wl,-Map,"project.map" -specs=nano.specs -specs=nosys.specs -o “project.elf" ./Sources/main.o ./Sources/memory.o ./Sources/ports.o ./Sources/timer.o ./Project_Settings/Startup_Code/startup_MKL25Z4.o ./Project_Settings/Startup_Code/system_MKL25Z4.o
Need something to simplify this!

## Slide 8: Build Management Software [S4]
Build Management Software (or Build Automation) provides a simple and consistent method for producing a target executable
Automated the process of
  Preprocessing
  Assembling
  Compiling
  Linking
  Relocating
Build System
Compiler
Object Files
Linker
Locator
Relocatable File
Executable
Assembler
Linker File
*.c
*.c
*.c
*.h
*.c
*.c
*.s
*.c
*.c
*.o
*.c
*.c
*.o
*.c
*.c
*.a
Library
Files
Notes: https://www.gnu.org/graphics/agnuhead.html

## Slide 9: GNU Compiler Collection [S5]
GNU Toolset performs all operations using make
  Preprocessing
  Assembling
  Compiling
  Linking
  Relocating
Build System
Compiler
Object Files
Linker
Locator
Relocatable File
Executable
Assembler
Linker File
*.c
*.c
*.c
*.h
*.c
*.c
*.s
*.c
*.c
*.o
*.c
*.c
*.o
*.c
*.c
*.a
Library
Files
Notes: Emphasize differences between an MCU and a Embedded OS

## Slide 10: GNU Make [S6]
GNU Make
  “Tool that controls the generation of executables and other non-source files of a program from the program’s source files.”2
GNU = GNU’s Not Unix
  A collection of software, a Toolset
  Contains GCC = GNUs Compiler Collection
Make is our Build Management Software
  Determines what files need to be compiled/recompiled in a project given a makefile
  Helps generate build dependencies and other files
  Widely used and free
Notes: [picture] https://www.gnu.org/graphics/agnuhead.html
[2] GNU Make. Website. https://www.gnu.org/software/make/. 27 January 2016.

## Slide 11: GNU Toolchain [S7a]
Source Files
Compiler
Linker
Locator
Relocatable File
Executable
Assembler
Linker File
*.c
*.c
*.c
*.h
*.c
*.c
*.s
*.c
*.c
*.o
*.c
*.c
*.o
*.c
*.c
*.a
GNU Make
Makefile
Notes: Emphasize differences between an MCU and a Embedded OS

## Slide 12: Makefiles [S8]
One or more files used to tell make how to build a particular project
  Invoked from the command line
Makefiles have build targets or build rules
  These are recipes for how to build a particular executable or non-source file
Executables can have dependencies
  Requirements needed for a particular recipe
  These can be auto-generated from make
Can define variables/constants to use during compilation
  Compiler Instance
  Compiler/Linker Options
  Architecture to build for
12
Compile Time Switch
Notes: ARM = Acorn RISC Machine – All risc processors
Risc examples: ARM, MIPS, SPARC, IBM Power PC, AtmelAVR
Cisc Examples: x86, AMD, Motorolla 68k, PDP
Give an example of reasons to have the two different:
-Lots of specialized instructions which give some type of speed or efficiency boost, incorporate many operations with lds/strs
-a reduced Common set of instructions (frequently used)
One instruction set computer, minimal instruction set computer, very long instruction word (VLIW)

## Slide 13: Makefile Rules/Targets [S9]
Many multiple rules can be executed for any given instance of make that is run
  Specify target you wish to execute when invoking make
  $ make main.o
  $ make all
  $ make clean
If no target is specified, defaults to first defined target in the makefile
$ make
13
Example Makefile Targets
Notes: ARM = Acorn RISC Machine – All risc processors
Risc examples: ARM, MIPS, SPARC, IBM Power PC, AtmelAVR
Cisc Examples: x86, AMD, Motorolla 68k, PDP
Give an example of reasons to have the two different:
-Lots of specialized instructions which give some type of speed or efficiency boost, incorporate many operations with lds/strs
-a reduced Common set of instructions (frequently used)
One instruction set computer, minimal instruction set computer, very long instruction word (VLIW)

## Slide 14: GNU Compiler Collection [S10]
GNU Make
Source Files
Compiler
Object Files
Linker
Locator
Relocatable File
Executable
Assembler
Linker File
*.c
*.c
*.c
*.h
*.c
*.c
*.s
*.c
*.c
*.o
*.c
*.c
*.o
*.c
*.c
*.a
Makefile
Notes: Emphasize differences between an MCU and a Embedded OS

## Slide 15: Build System [S11]
GNU Make
Source Files
Object Files
*.o
*.o
*.o
Map Files
Executable
Linker File
Makefile(s)
Generated Files
*.c
*.c
*.c/*.h
*.c
*.c
*.s
*.c
*.c
*.a
Dependency Files
$ make all
Notes: Many of these steps are combined in one operation

## Slide 16: IDE and Make Autogeneration
Your IDE typically will list Makefiles, output files, and executables in the project explorer
IDE will dynamically create Makefiles through the use of file auto-generation
  Software teams DO NOT use IDE autogenerated build systems, they create their own
Kinetis Design Studio Make Build System
Banner that gets inserted at the top of all of your auto-generated files

## Slide 17: IDE and Make Autogeneration
Banner that gets inserted at the top of all of your auto-generated files
Your IDE typically will list Makefiles, output files, and executables in the project explorer
IDE will dynamically create Makefiles through the use of file auto-generation
  Software teams DO NOT use IDE autogenerated build systems, they create their own
Kinetis Design Studio Make Build System